## Slide 1: The Last-Level Branch Predictor
David Schall1*, Andreas Sandberg2, Boris Grot1
University of Edinburgh1, Arm Ltd2
Nov. 4, 2024
*Now at TU Munich

## Slide 2: Branch Prediction
Essential for modern CPU’s
Unlocks more aggressive processor designs [Intel’19]
Key limiter for performance
  Mispredictions waste
    tens of cycles and hundreds of instructions
    9.2% of execution cycles on Intel Sapphire Rapids
    15.4% of executing cycles in Googles data centres [Google’19]
Branch mispredictions are a key bottleneck for modern processors
Execution cycles wasted due to branch misprediction
Wasted cycles [%]

## Slide 3: State-of-the-art in Branch Prediction
TAGE (TAgged GEometric history length)
Partial pattern-matching with global history
Multiple tables for different lengths of histories
Upon misprediction, allocates a pattern with a longer history
Implemented in many commercial CPU’s
Arm, IBM, Qualcomm,…
How does TAGE perform on modern server workloads?
PC
Hn
prediction
prediction
PC
H2
PC
H1
Short History
…
Long History
Predictor Pattern
0
1
1
0
0
0
0
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
Global Branch History
0
1
0
0
0
1
0
0
1
0
0
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
…
?
Next branch

## Slide 4: TAGE in the Limit
Baseline 64KiB TAGE-SC-L (TSL) (state-of-the-art)
High number of mispredictions (avg. 2.9 MPKI, max. 6.4 MPKI)
 Flush every ~300 instructions
Compare Intel Sapphire Rapids ROB: 512-entries
TAGE with unlimited capacity (Inf TAGE)
Reduces mispredictions by 32%
A larger TAGE significantly reduces mispredictions
Lower is better

## Slide 5: Understanding the Branch Working Set
Studied the execution of 13 server workloads
Analyzed mispredictions & useful patterns for individual branch instructions
Two key insights:
Mispredictions are skewed
  Hard-to-predict (H2P) (<1% of all branches)…
  …responsible for >40% of all mispredictions
  …offer >1/3 of the opportunity with more capacity
H2P
H2P
(Hard-to-predict)
All Branches
All Mispredictions
H2P
(Hard-to-predict)

## Slide 6: Understanding the Branch Working Set
Studied the execution of 13 server workloads.
Analyzed mispredictions & useful patterns for individual branch instructions
Two key insights:
Mispredictions are skewed
  Hard-to-predict (H2P) (<1% of all branches)…
  …responsible for >40% of all mispredictions
  …offer >1/3 of the opportunity with more capacity
Branch working set is skewed
  Most branches consume only few patterns
    Combined patterns of tens of thousands of simple branches
  H2P branches 100-1000s of patterns per branch
Takeaways:
Need to address both simple and hard-to-predict branches
Multiple KBs per H2P branch are needed
prediction

## Slide 7: Jacking up the Branch Predictor
Option 1: Up-scaling TAGE tables
Increases table access latencies
   Offsets accuracy gains [HPCA’03]
Practical limits to increase the tables
Up-scaling TAGE tables is counterproductive
prediction

## Slide 8: Jacking up the Branch Predictor
Option 2: Hierarchical TAGE
  Branch Predictor hashes PC with branch history
  which creates two problems:
  Many patterns per branch possible
    Simple branches: Few patterns
    H2P branches: 100-1000s patterns
      Impossible to move multiple kilo-bytes per branch
  Breaks locality
    Patterns cannot be associated with its branch PC
    Impedes prefetching
No conventional technique to build hierarchical branch predictors!
prediction
PC = ?
PC = ?

## Slide 9: Towards a Hierarchical Branch Predictor
Approach:
  Identify the subset of patterns needed for the upcoming branch execution
  Prefetch just those patterns
Challenge:
Localize patterns for an upcoming branch execution
prediction

## Slide 10: Introducing Contexts
fnC
fnB
fnA
Observations:
H2P branches have patterns with long history
Span multiped code regions (e.g. function calls)
Sequence of unconditional branches identify global program state  program context (aka. call chain)
1
1
0
0
1
1
0
1
0
0
1
1
0
0
0
0
1
0
1
1
0
1
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
?
H2P branch
Global History
CallA
CallB
CallC
fnA
CallA
fnB
CallB
fnC
CallC
Program Context
1
1
0
1
1
…
…
H2P
Long history pattern

## Slide 11: Introducing Contexts
Hypothesis:
Branch behaviour can be captured per context
  Sequence of preceding unconditional branches identify context
   Context locality
1
1
0
0
1
1
0
1
0
0
1
1
0
0
0
0
1
0
1
1
0
1
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
Pattern 1
1
1
0
0
1
1
0
0
1
1
1
0
0
0
1
0
1
0
1
0
1
0
0
0
1
1
0
1
1
1
0
1
0
0
1
1
0
1
0
Pattern 2
1
1
1
0
1
1
0
1
0
1
1
1
1
1
0
0
0
1
0
1
0
1
1
0
0
1
0
1
1
1
1
1
0
1
0
0
1
1
0
Pattern 3
1
1
0
0
1
1
0
0
0
1
1
0
0
0
0
1
0
0
1
1
0
1
0
0
1
1
0
1
1
1
0
1
0
0
1
0
0
1
0
Pattern 4
0
1
0
0
1
1
0
1
0
1
0
0
0
0
1
0
1
0
1
1
0
0
0
0
1
1
0
1
1
1
0
1
0
0
0
0
0
1
0
Pattern 5
Context ABC
fnA
fnB
fnC
H2P
fnD
fnE
fnF
Context DEF
Context ABC
Context DEF

## Slide 12: Introducing Contexts
Hypothesis:
Branch behaviour can be captured per context
  Sequence of preceding unconditional branches identify context
   Context locality
The larger the context depth the fewer patterns per context
1
1
0
0
1
1
0
1
0
0
1
1
0
0
0
0
1
0
1
1
0
1
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
Pattern 1
1
1
0
0
1
1
0
0
1
1
1
0
0
0
1
0
1
0
1
0
1
0
0
0
1
1
0
1
1
1
0
1
0
0
1
1
0
1
0
Pattern 2
1
1
1
0
1
1
0
1
0
1
1
1
1
1
0
0
0
1
0
1
0
1
1
0
0
1
0
1
1
1
1
1
0
1
0
0
1
1
0
Pattern 3
1
1
0
0
1
1
0
0
0
1
1
0
0
0
0
1
0
0
1
1
0
1
0
0
1
1
0
1
1
1
0
1
0
0
1
0
0
1
0
Pattern 4
0
1
0
0
1
1
0
1
0
1
0
0
0
0
1
0
1
0
1
1
0
0
0
0
1
1
0
1
1
1
0
1
0
0
0
0
0
1
0
Pattern 5
Context GABC
fnA
fnB
fnC
H2P
fnD
fnE
fnF
Context HDEF
fnG
fnH
fnI
Context IDEF
Context GABC
Context HDEF
Context IDEF

## Slide 13: Confirming Contexts
Method:
Create context by hashing uncond. branch instructions
  Aka. Hash of the call chain
Count useful patterns per context
Increase context depth (number of branches hashed)
Finding:
The more unconditional branches are hashed to form the context,…
…the fewer patterns per context are needed to predict a branch
Contexts localize a small subset of patterns useful to predict a branch

## Slide 14: The Last-Level Branch Predictor (LLBP)
LLBP: Stores patterns organized per context (Pattern Set)
Pattern Buffer: Makes predictions from current active pattern set
Context directory: Identifies and prefetches pattern sets for upcoming contexts
LLBP
(Pattern Store)
  Context-sensitive branch predictor storage augmenting TAGE
Core Front-end
Pattern Buffer
prediction
Context Directory
Context
ID
LLBP .
(Pattern Store)
TAGE
Pattern Set
…

## Slide 15: The Last-Level Branch Predictor (LLBP)
Core Front-end
Prediction:
Create Context ID upon executing uncond. branch
Context directory hit triggers prefetch
Pattern buffer make predictions from current active context
Associate current context with future context to overcome LLBP access latency
LLBP
(Pattern Store)
Pattern Buffer
prediction
Context Directory
Context
ID
LLBP .
(Pattern Store)
TAGE
…
  Context-sensitive branch predictor storage augmenting TAGE
Context
ID
fnA
CallA
fnB
CallB
fnC
CallC
H2P

## Slide 16: The Last-Level Branch Predictor (LLBP)
Core Front-end
Training:
Upon misprediction a new pattern is allocated in TAGE and LLBP (same pattern)
Create new pattern set if none exists for current context
As patterns get replaced in TAGE, LLBP still preserves them due to larger capacity
LLBP
(Pattern Store)
Pattern Buffer
prediction
Context Directory
Context
ID
LLBP .
(Pattern Store)
TAGE
  Context-sensitive branch predictor storage augmenting TAGE
Context-based organization enables hierarchical branch predictor designs

## Slide 17: Results
LLBP:
Reduces mispredictions by 8.9% over 64 KB TAGE-SC-L
Achieves ~33% of ideal TAGE with similar storage budged (512KB)
Unlocks new innovations in branch predictor designs
Higher is better

## Slide 18: Takeaways
Branch predictions remains a key performance limiter for modern CPU’s
  >9% of execution cycles are wasted due to branch mispredictions
Analysis shows significant opportunity with larger predictor structures
  Additional latency impedes larger predictor structures
  No conventional technique to build hierarchical branch predictors
  Introduce context locality
  Localize a small subset of patterns for given branch execution
  Enables hierarchical branch predictor designs
LLBP: Context-based, hierarchical branch predictor organization
  Improves branch prediction accuracy by 8.9%

## Slide 19
Thank you!
Extensive characterization
Design details
Sensitivity studies
LLBP implementation
https://github.com/dhschall/LLBP/