## Slide 1
The Last-Level Branch Predictor Revisited
David Schall1, Mária Ďuračková2, Boris Grot2
Technical University of Munich1, University of Edinburgh2
Feb. 3, 2026

## Slide 2: Branch Prediction
Essential for modern CPUs
Mispredictions waste
  tens of cycles and hundreds of instructions
  15.4% of executing cycles in Google’s data centres [Google’19]
Unlocks aggressive processor designs
Aggressive pipelines shift bottleneck to the branch predictor [Intel’19]
Skylake (2015)  Sapphire Rapids (2025)
  Massive pipeline upscale: Width: 58 (1.6x), ROB 224512 (2.3x)
  Significant reduction in mispredictions  ~35%
  But fraction of branch-related stalls increased  ~5%
Branch mispredictions are a key performance killer
Wasted cycles [%]
Branch MPKI
Lower is better

## Slide 3: The TAGE Branch Predictor
TAGE (TAgged GEometric history length)
Partial pattern-matching with global history
Stores patterns (Hash of PC + history) in matching tables
Multiple tables for different lengths of histories
Upon misprediction, allocates a pattern with a longer history
TAGE-SC-L state-of-the-art since >10 years
TAGE + perceptron + loop predictor
Implemented in many commercial CPU’s
Arm, IBM, Qualcomm,…
PC
Hn
prediction
prediction
PC
H2
PC
H1
Short History
…
Long History
0
1
1
0
0
0
0
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
Global Branch History
0
1
0
0
0
1
0
0
1
0
0
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
…
?
Next branch
What are the challenges with TAGE?
Prediction counter
Useful bit
ctr
u
tag
Prediction pattern
Hash(PC, GHR)

## Slide 4: The Capacity-Latency Trade-off
Branch predictor is in the critical fetch path  must be accurate & fast
Larger predictors improve accuracy
More capacity allows storing more patterns
 Captures more correlations
64K TAGE-SC-L  512K TSL (8x capacity)
 Reduces mispredictions by 27% 🙂
Lower is better
How to increase predictor capacity without additional latency?
Larger predictors hit physical limits
High prediction latency
High energy consumption
 Offsets accuracy gains!
☹️
impractical

## Slide 5: The Last-Level Branch Predictor (LLBP) [MICRO ‘24]
Approach: Hierarchical branch predictor
Pattern Store: large but slow capacity structure to store patterns
Pattern Buffer: small and fast structure to make predictions
Prefetch required patterns into pattern buffer for upcoming predictions
  Context-sensitive branch predictor storage augmenting TAGE
Core Front-end
Pattern Buffer
prediction
LLBP .
(Pattern Store)
TAGE
…
How to know which patterns are needed ahead of time?
???
Context Directory
Context
ID

## Slide 6: Enabling Hierarchical Branch Predictors via Contexts
Observations:
Branches can have many patterns with long history (hundreds of branches)
Span multiple code regions (e.g. function calls)
Sequence of unconditional branches identifies global program state
 program context (aka. call chain)
fnC
fnB
fnA
1
1
0
1
1
1
0
1
0
0
1
1
0
0
0
0
1
0
1
0
1
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
?
branch
Global History
CallA
CallB
CallC
fnA
CallA
fnB
CallB
fnC
CallC
Program Context  ABC
…
…
br
Pattern 1
1
1
1

## Slide 7: Enabling Hierarchical Branch Predictors via Contexts
fnC
fnB
fnA
Observations:
Branches can have many patterns with long history (hundreds of branches)
Span multiple code regions (e.g. function calls)
Sequence of unconditional branches identifies global program state
 program context (aka. call chain)
br
fnD
fnC
fnB
fnD
1
1
0
0
1
1
0
1
0
0
1
1
0
0
0
0
1
0
1
0
1
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
?
branch
Global History
CallD
CallB
CallC
Program Context  DBC
…
…
Pattern 1
0
0
1
1
1
1
0
0
1
1
0
1
0
0
1
0
0
1
0
1
1
1
0
1
0
0
1
0
0
1
0
?
Pattern 2
Contexts can identify required patterns ahead of time
fnA
CallA
fnB
CallB
fnC
CallC
CallD

## Slide 8: Enabling Hierarchical Branch Predictors via Contexts
LLBP Mechanism:
Group patterns per context into pattern sets
Form context ID by hashing uncond. branches
br
fnD
fnA
CallA
fnB
CallB
fnC
CallC
CallD
01010001
01011101
ABC
DBC
ABC
DBC

## Slide 9: Enabling Hierarchical Branch Predictors via Contexts
Core Front-end
Pattern Buffer
prediction
Context Directory
Context
ID
LLBP .
(Pattern Store)
TAGE
How effective is LLBP?
Context
ID
LLBP Mechanism:
Group patterns per context into pattern sets
Form context ID by hashing uncond. branches
Use context ID to prefetch pattern sets
DBC
br
fnA
CallA
fnB
CallB
fnC
CallC
ABC

## Slide 10: LLBP Effectiveness
Compare 512K LLBP with 512K TSL
LLBP reduces mispredictions by 8.8% over 64K TSL
Only 1/3 of the reduction of a similarly sized (but impractical) TAGE-SC-L (512K TSL)
What affects LLBPs’ effectiveness and can it be improved?
Higher is better

## Slide 11: Outline
To understand & address LLBP’s limitations we:
Performed root-cause analysis of LLBP’s inefficiencies
 Identified two main compounding negative effects
Developed mechanism to overcome both limitations
   Unified and light-weight solution

## Slide 12: Understanding LLBP’s Bottlenecks
Problem 1: Skewed pattern set utilization
LLBP organization: 14k pattern sets, each with up to 16 patterns
Most pattern sets are underutilized
    85% of the sets have less than 16 useful patterns
Some pattern sets are heavily overutilized
    15% of the sets require more than 16 patterns, and a few up to 1k
underutilized
overutilized
LLBP’s fixed-size pattern sets result in wasted capacity and lost coverage
LLBP storage
16 x 14k

## Slide 13: Understanding LLBP’s Bottlenecks
Problem 2: Pattern duplication due to contextualization
LLBP uses a fixed context depth
  Number of unconditional branches to create the context ID
Context too deep for patterns with short history
  The same pattern must be replicated in multiple pattern sets
  Wastes capacity and increases training time
Deep context depth requires duplication of short history patterns
br
fnD
fnA
CallA
fnB
CallB
fnC
CallC
ABC
DBC
fnC
fnB
fnA
0
0
0
1
?
fnD
1
1
1
1
1
0
0
1
1
0
1
0
0
1
0
0
1
0
1
1
1
0
1
0
Context Depth (3 UBs)
Pattern History Length (4 Branches)
1
1
1
0001
0001
Context Depth (3 UBs)

## Slide 14: Addressing LLBPs Inefficiency
Key Problems:
Skewed pattern set utilization
Pattern duplication due to contextualization
Naïve Approach: Change LLBP organization
E.g., multiple types of pattern sets, chaining if overflow,…
However:
    Implementation challenges, multiple LLBP lookups, or higher bandwidth
    Doesn‘t solve pattern duplication
How can we overcome both limitations without changing the pattern set organization?

## Slide 15: Addressing LLBPs Inefficiency
Key Problems:
Skewed pattern set utilization
Pattern duplication due to contextualization
Our Idea: Dynamic context depth
Use shallow context depth by default
  Coarse-grained contextualization
  Increase utilization of underutilized sets
  Reduces pattern duplication
Increase depth when pattern set becomes full
  Fine-grained contextualization
  Splits overutilized pattern sets into multiple sets
br
fnD
fnA
fnB
CallB
fnC
CallC
ABC
DBC
C
CallA
0101
1101
0011
0001
0101
10011
One solution to overcome both limitations
Context Depth (1 UB)
Context Depth (3 UBs)

## Slide 16: LLBP-X
Dynamic context depth adoption
Context tracking table (CTT) monitors highly contended pattern sets
Upon exceeding a threshold, CTT switches to use a deep context
  Effectively spreads patterns across more pattern sets
NO change to LLBPs’ storage organization needed
Unified solution for both limitations
CTT increases LLBPs’ storage and energy by less than 2%
Core Front-end
Pattern Buffer
prediction
LLBP .
(Pattern Store)
TAGE
LLBP-X is a simple and lightweight enhancement to LLBP
Context Directory
…
CTT
Shallow
CID
Deep
CID

## Slide 17: Results
LLBP-X’s lightweight adaptation mechanism significantly improves efficiency
12.1% misprediction reduction over 64K TSL
27% more effective than LLBP
  With less than 2% storage and energy overhead over LLBP
Achieves 45% of the accuracy increase compared to ideal 512K TSL
LLBP-X is simple and effective
Higher is better

## Slide 18: Takeaways
Branch predictions remains a key performance limiter for modern CPU’s
Larger predictors significantly reduce mispredictions
But predictor latency impedes larger predictors
LLBP addresses the capacity-latency trade-off with hierarchical design
However, falls far behind equally sized (but impractical) 512K TSL
Detailed root-cause analysis revealed key inefficiencies of LLBP
Skewed pattern sets utilization
Pattern duplication due to contextualization
LLBP-X: Dynamic context depth adaptation
Simple and lightweight enhancement of original design
Improves effectiveness of LLBP by 27%

## Slide 19
Thank you!
Extensive characterization
Design details
Sensitivity studies
LLBP-X implementation
(CBP & gem5)
https://github.com/dhschall/LLBP-X/